## Slide 1: Reservoir model
Jan. 2018

## Slide 2: Simplified 2-reservoir model (image/data from PCWA)

## Slide 3
Middle Fork American River
Rubicon River
Duncan Creek Diversion
Hell Hole Reservoir
207.6 TAF
French Meadows Reservoir
136.4 TAF
French Meadows Powerhouse
15.3 MW
Middle Fork Powerhouse
122.4 MW
Environmental flow requirements
Environmental flow requirements

## Slide 4: Daily flow data from USGS
Only French Meadows inflow is changed by the hydrologic modeling
Model period 10/1/1980 – 9/30/2015
Model assumes env. flows met first
Then, hydropower production is calculated using a linear storage-elevation curve

## Slide 5: Year-round instream flow requirements

## Slide 6: Pulse flow requirements
Second, add pulse flows. 4 scenarios:
No pulse (only instream flows)
FERC proposed (“FERC”)
+1 day/step, +10% cfs/day (“increase”)
Same, plus a <20% restriction on rampdown (“increase_rampdown”)
Only apply to W/AN year types

## Slide 7: Fitting the historical release policy
To run other scenarios, we first have to represent the hydropower release policy
Approximated from observed historical data, assuming a set of “if-then” rules based on storage and day of the year

## Slide 8: Two experiments:
How much hydropower is generated under different hydrologic scenarios, if the release policy stays the same?
What if the release policies are re-optimized to each hydrologic scenario?